## Slide 1: Smart Transmission
Aaron Grant
Horatio Cowan
Molly Segee
Carl Burnham

## Slide 2: Schedule
January: Ordering Parts & beginning fabrication
February: Continuing fabrication & Assembly
March: Assembly and Initial Testing
April: Coding & Calibration
May: Presentation

## Slide 3: Parts
qty | part | Status
1 | 2004 Honda TRX 450R | Arrived
1 | 3-Wire Extension Cables (Large Bundle) P/N: 276-1424 | Arrived
2 | IFI VEX Pro Victor 888, Part number: 217-2769 | Arrived
1 | 6-POSITION ATO/ATC FUSE PANEL WITH COVER AND COMMON GROUND: Product number: WIRTH-31060 | Arrived
3 | Fuse ATC Standard Blade Auto 3 Amp Violet: Product number: FU-509123 | Arrived
3 | Fuse ATC Standard Blade Auto 15 Amp Blue: product number: FU-509128 | Arrived
3 | Fuse ATC Standard Blade Auto 25 Amp Clear: Product number: FU-509130 | Arrived
7 | Wire 8 Gauge Red Sold by the foot Product Code #: WI-230702 | Arrived
7 | Wire 8 Gauge Black Sold by the foot Product Code #: WI-230700 | Arrived
10 | Lug Straight Heavy Duty 8 GA #10 Hole Product Code #: LU-1800HD | Arrived
10 | Lug Straight Heavy Duty 8 GA 1/4" Hole Product Code #: LU-1801HD | Arrived
20 | Connector Nylon Tab Insulated Female, .250" Blade 16-14 GA, Blue Product Code #: CT-163258 | Arrived
15 | Connector Nylon Tab Insulated Male, .250" Blade 16-14 GA, Blue Product Code #: CT-163260 | Arrived
10 | Connector Premium Nylon #6 Ring Terminal Double Crimp 16-14 AWG Blue Product Code #: CT-163202 | Arrived
1 | Dual USB Power Hub 2 Amp product code: 22-1-39290-8 | Arrived
1 | All Weather 12 Volt Power Socket, product code: 22-1-39052-8 | Arrived
1 | Slide Potentiometers 60mm TRVL Linear 10K Part #: 312-9301F-10K | Arrived
1 | Tubular High-Speed Linear Actuator (Stroke Size 3", Force 11 lbs, Speed 9.05"/sec), Part number: PA-15-3-11 | Arrived
1 | Electrak Pro PR12-02-2A65-02-LSB Linear Actuator | Returning
1 | Adafruit Assembled Data Logging shield for Ardino, ID: 1141 | Arrived
1 | Arduino Mega 2560 R3 (Atmega2560 - assembled) ID 191 | Arrived
2 | Panel Mount 10K potentiometer (Breadboard Friendly) ID 562 | Arrived
2 | Arduino Uno R3 (Atmega328 -assembled) | Arrived
1 | Sensor Gear Tooth Hall Effect, Part number: 480-2021-ND | Arrived
1 | 12V, 1.6A, 233 oz-in Geared Bipolar Stepper Motor, product code: RB-Phi-131 | Arrived
1 | 50 AMP MANUAL-RESET DC CIRCUIT BREAKER BPC Item# 11-3317-50 | Arrived
1 | Arduino Motor Shield R3 | Arrived
2 | BYTECC USB2-3AB-K 3 ft. Type A Male to Type B Male Cable | Arrived
qty | Part |  |  |  |  |  |  | per | total | status
3 | Slide Potentiometers 60mm TRVL Linear 10K Part #: 312-9301F-10K |  |  |  |  |  |  | $2.55 | 7.65 | Ordered
4 | Thick Film Resistors - Through Hole 20watt 5.6ohms 1% Part #: 652-PWR220T-20-5R60F |  |  |  |  |  |  | $3.58 | 14.32 | Ordered
1 | 50 ft Standard Duty Servo Wire (Futaba) Part #: SW24J |  |  |  |  |  |  | $12.95 | 12.95 | Ordered
6 | OEM hitec male (Silver Pin) servo plug and pins |  |  |  |  |  |  | $2.99 | 17.94 | Ordered
1 | 2" Linear Actuator with Preset Limit Switch model #: 6102C |  |  |  |  |  |  | $151.0 | 151 | Ordered
1 | 12" × 24" 3/16" Clear Plastic Sheet Part #: 8560K219 |  |  |  |  |  |  | $20.14 | 20.14 | Ordered
 |  |  |  |  |  |  |  |  | 224 | total

## Slide 4: Mech Lab Experiment
We are acquiring engine, wheel speed, and throttle position data from sensors we have mounted on the 4-wheeler.
We will use this data to generate expressions to identify shift points and generate a curve fit which we can use for writing the program.
Chart: Wheel speed vs. throttle position at shift points
| 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200
first to second shift points | 103.3148 | 118.4025 | 135.4991 | 154.8721 | 176.8246 | 201.7 | 229.8875 | 261.8282 | 0.005 | 100 | -10
second to third gear shift points | 212.3668 | 249.9718 | 293.6624 | 344.4238 | 403.4 | 471.9206 | 551.5302 | 644.0234 | 0.006 | 200 | -20
third to fourth gear shift points | 267.8116 | 324.7669 | 392.6147 | 473.4382 | 569.7188 | 684.4128 | 821.0415 | 983.8 | 0.007 | 250 | -30
fourth to fifth gear shift points | 326.4208 | 407.5474 | 506.6356 | 627.6623 | 775.4845 | 956.0351 | 1176.56 | 1445.9097 | 0.008 | 300 | -40

## Slide 5: Data Logging Shield
Takes a standard SD card
Has its own real time clock and battery
Creates a new file each time it powers on.
Using the IDE we can write whatever sensor data we want, as many times per second as we want.
Files can then be opened in excel and analyzed.

## Slide 6: Engine Speed Sensor
Chart: First Engine speed sensor Data
The magnetic field lines move in the same direction as the wire. We aren’t getting enough electromagnetic magnetic flux.

## Slide 7: New engine speed inductor
Magnetic field lines are now transverse to the wire.
Chart: 

## Slide 8: Stepper Motor Control
Rated Current 1.7 amps
Coil Resistance 1.7 ohms
12V/1.7ohms= ~7 amps (Way higher than rated Current)
Stepper motor should not have more than 3 volts applied across it continuously.
Ideally a 5.35 Ω resistor should be used. (they don’t exist) Instead we found a 5.6 Ω.
Stepper Motors use Inductors. This is an LC circuit.
Inductors Charge up, eventually reaching a steady state current.
Because there is no voltage drop across the resistor, all of the voltage drop occurs across the inductor. This causes the inductor to charge up faster.
At time T=0, there is no current, and thus no voltage drop across the resistor.
The inductor now has the remaining 2.8 volts across it, and the current has not exceeded the rated amount.
Once the system has reached steady state, there will be 1.64 amps through the resistor which is a voltage drop of 9.2 volts
Conclusion: Using resistors will make it step faster without losing strength or risking damaging the stepper motor.

## Slide 9: Wiring on the 4-Wheeler

## Slide 10: Attaching the stator to the battery

## Slide 11: Battery Mount

## Slide 12: Circuit Breaker Attachment

## Slide 13: Circuit Breaker Attachment

## Slide 14: Fuse Box Attachment

## Slide 15: LCD screen

## Slide 16: LCD mount

## Slide 17: Sensor Power Distribution

## Slide 18: Control Box

## Slide 19: Control Box Mount

## Slide 20: Wheel speed sensor mounted, wired, and tested.

## Slide 21: Throttle Position Sensor

## Slide 22: Throttle Position Sensor Design

## Slide 23: Throttle Position Sensor Fabrication

## Slide 24: Shifter Peg Actuation

## Slide 25: Shifter Peg Actuator Mount Design

## Slide 26: Shift Peg Actuator Potentiometer Mount

## Slide 27: Shift Peg Actuator Fabrication

## Slide 28: Shift Peg Actuation Assembly

## Slide 29: Throttle Cable Actuator: Previous Presentation

## Slide 30: Throttle Cable Actuator Refined Design

## Slide 31: Throttle Cable Actuator Finished and Mounted

## Slide 32: Everything so far

## Slide 33
Questions?